## Slide 1
Department of Computer Engineering and Technology (SCET)
Computer Networks (CET2005B)

## Slide 2: Computer Networks: COURSE STRUCTURE

## Slide 3: Pre-requisites
Programming and Problem Solving
Principles of Programming Languages with Python Programming
Object Oriented Programming with C++

## Slide 4: Syllabus
1 | Fundamentals of networking and data communication (9 Hrs) Analog Transmission: Analog-to-Analog conversion, Digital-to-Analog conversion, Digital Transmission: Digital-to-Digital conversion (line coding, block coding, scrambling), Analog-to-Digital conversion (Pulse Code Modulation, Delta Modulation) Types of Networks, Network Architectures, Network Topologies, Transmission media’s, Networking devices, OSI Model, TCP/IP Reference Model, Ethernet standards.
2 | Data Link Layer: (9 Hrs) Data Link Layer Services, Types of errors, Block coding, Error Control: Cyclic Redundancy Check (CRC) Code, Hamming Code, Checksum, sliding window Protocols: Selective Repeat (SR) & Go Back N (GBN), Channel allocation, Multiple Access Protocols: ALOHA, CSMA/CD, CSMA/CA, Ethernet Frame format.
3 | Network Layer (9 Hrs) Services, Internet Protocol: Ipv4 & Ipv6, Classful Addressing, Classless Addressing, CIDR, Subnetting, NAT, ARP, RARP ICMP, Routing Algorithms: Distance-Vector (DV) Routing, Link State (LS) Routing, Routing in Internet: RIP, OSPF, BGP
4 | Transport Layer (9 Hrs) Services, Multiplexing, demultiplexing. Sockets, UDP, RTP, TCP: Services, Features, Segment, TCP Connection (Three-Way Handshake), Flow control and buffering, Silly window syndrome, Congestion Control. Congestion Control (Leaky Bucket, Token Bucket), Quality of Service (QoS)
5 | Application Layer (9 Hrs) Dynamic Host Control Protocol (DHCP), Hypertext Transfer Protocol (HTTP), FTP, TELNET, SMTP: POP3, IMAP, MIME, Domain Name System (DNS), SNMP.

## Slide 6: Guidelines for CCA and LCA
Examination Scheme
CCA Marks Distribution
Sr. No. | Examination Scheme | Marks
1. | Class Continuous Assessment (CCA) | 30
2. | Laboratory Continuous Assessment (LCA) | 30
3. | Term End Examination | 40
Sr. No. | Class Continuous Assessment: (30 Marks) | Marks
1. | Mid Term Exam | 15
2. | Active Learning | 10
3. | Theory Assignment | 05
Sr. No. | Laboratory Continuous Assessment: (30 Marks) | Marks
1. | Practical Performance | 10
2. | Active learning / Mini Project/ Additional implementation | 10
3. | End Term Practical/ Oral Examination | 10

## Slide 7
Lab Assignment
Study different Linux networking commands. 2Hrs
Design a Network:( Design a simple network (LAN) with different topologies & test it using PING utility. 2 Hrs
Configure VLAN: Design and configure a virtual LAN. 2Hrs
Implement Error Control Protocol: ( Write a program for error detection and correction codes using Hamming Codes. 4 Hrs
Subnetting: Write a program to implement subnetting to find subnet mask 2Hrs
Static and Dynamic NAT Configuration: Implement Static and Dynamic NAT Configuration with Packet Tracer. 2Hrs
Configuration of Routing Protocol: Set up a network - configure interfaces, IP addresses and routing protocols (RIP, OSPF, EIGRP, BGP).
TCP socket Programming: Write a C program for wired network using TCP socket to demonstrate a) Chat Application (50% Students) b) Mathematical operations. (Remaining 50% Students) Show packet captured traces using Wireshark Packet Analyzer Tool. (4 Hrs)
UDP Socket Programming: (Language: C/C++/Python/Java)/ Write a C program for wired network using UDP socket to perform any one of the following operations. (4 Hrs)
a. String Conversion from Uppercase to Lowercase. (50% Students)
b. Reverse the String. (Remaining 50% Students) Show packet captured traces using Wireshark Packet Analyzer Tool. (4 Hrs)
DHCP and DNS Configuration: Configure network using Dynamic Host Configuration Protocol (DHCP), DNA and Web server Use Ping utility to test connectivity. (4 Hrs)

## Slide 8
Unit I: Fundamentals of Networking and Data Communication
Analog Transmission: Analog-to-Analog conversion, Digital-to-Analog conversion.
Digital Transmission: Digital-to-Digital conversion (line coding, block coding, scrambling), Analog-to Digital conversion (Pulse Code Modulation, Delta Modulation)
Types of Networks, Network Architectures, Network Topologies,
Transmission media’s, Networking devices, OSI Model, TCP/IP Reference Model,
Ethernet standards.

## Slide 9
Text Books:
1. Behrouz A. Forouzan, ‘Data Communications and Networking’, 5th Edition, McGrawHill Publishing Company, ISBN 978-0-07-337622-6
2. Tanenbaum A. S., ‘Computer Networks’, Pearson Education, 5th Edition, ISBN-978-0-13-212695-
Reference Books:
1. James F. Kurose and Keith W Ross ‘Computer Networking, A Top-Down Approach’, 5th Edition, Pearson Education, ISBN- 978-81-317-9054-0
2. W. Richard Stevens, Unix Network Programming, The Sockets Networking API, Vol 1, 3rd Edition, PHI Learning Pvt. Ltd.
Supplementary Reading:
1. William Stallings, ‘Data and Computer Communications’, 6th Edition, Prentice Hall of India Pvt.
Learning Resources:

## Slide 10
Introduction
Data Communications Telecommunication – means communication at a distance. (“tele”, Greek word for “far”)
Data - refers to information presented in whatever form is agreed upon by the parties creating and using the data
Data Communication - exchange of data between two devices via some form of transmission medium such as a wire cable
Data is a collection of facts. Information is how you understand those facts in context
Data is unorganized, while information is structured or organized.
Data is not typically useful on its own, but information is.
Information depends on data.

## Slide 12
Data Transmission
Data Transmission
Analog Transmission
Analog data Analog transmission
Digital data Analog transmission
Digital Transmission
Digital data Digital transmission
Analog data Digital transmission
AM
FM
PM
ASK
FSK
PSK
Line Coding
Block Coding
Scrambling
PCM
DM

## Slide 13
Characteristics of Waveform

## Slide 14
Analog and Digital Data
The term analog data refers to information that is continuous.
Analog data, such as the sounds made by a human voice, take on continuous values can be captured by a microphone and converted to an analog signal or sampled and converted to a digital signal.
Digital data refers to information that has discrete states.
Digital data take on discrete values. For example, data are stored in the memory as 0s and 1s.
They can be converted to a digital signal or modulated into an analog signal for transmission across a medium.

## Slide 15
Analog and Digital Signals
Signal - A signal is an electromagnetic or electrical current that is used for carrying data from one system or network to another.
An analog signal is any continuous signal for which the time varying feature of the signal is a representation of some other time varying quantity i.e., analogous to another time varying signal.
A digital signal is a signal that represents data as a sequence of discrete values; at any given time it can only take on one of a finite number of values.
Discrete value 1 and 0.

## Slide 16
Difference between Analog and Digital Signals
Analog Signals | Digital Signals
Analog signal is continuous and time varying. | Digital signal have two or more states and in binary form.
Troubleshooting of analog signals are difficult. | Troubleshooting of digital signals are easy.
An analog signal is usually in the form of sine wave. | An digital signal is usually in the form of square wave.
Easily affected by the noise. | These are stable and less prone to noise.
Analog signals use continuous values to represent the data. | Digital signals use discrete values to represent the data.
Accuracy of the analog signals may be affected by noise. | Accuracy of the digital signals are immune from the noise.
Analog signals may be affected during data transmission. | Digital signals are not affected during data transmission.
Analog signals use more power. | Digital signals use less power.
Examples: Human voice, natural sound, Audio signal, Radio signal etc. | Examples: Computers, Optical drives, etc.
Components like resistors, Capacitors, Inductors are used in analog circuits. | Components like transistors, logic gates, and micro-controllers are used in Digital circuits.

## Slide 17
Period and Frequencies
Period refers to the amount of time, in seconds, a signal needs to complete 1 cycle.
Frequency refers to the number of periods in 1 s
Frequency and period are the inverse of each other.

## Slide 18
Period and Frequencies
Example 1. The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 2. The period of a signal is 100 ms. What is its frequency in kilohertz?
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 19
Modulation
Modulation is the process of altering one or more properties of a periodic waveform known as a carrier signal with respect to the modulating signal, which contains information to be transmitted.
Modulation is performed by the device known as a modulator, and this technique is mainly used to overcome the interference of the signal.
Modulation techniques typically aid in long-distance communication.
Modulation is of two types:
1. Analog Modulation
2. Digital Modulation

## Slide 20
Types of Analog-to-Analog Modulation
Amplitude Modulation: Amplitude is varied keeping Frequency and Phase constant.
Frequency Modulation: Frequency is varied keeping Amplitude and Phase constant.
Phase Modulation: Phase is varied keeping Amplitude and Frequency constant.
Amplitude is varied
Frequency is varied
Phase is varied

## Slide 21
Amplitude Modulation
The total bandwidth required for AM can be determined from the bandwidth of the audio signal: BAM = 2B.
An oscillator is a circuit which produces a continuous, repeated, alternating waveform without any input.
Amplitude is varied keeping frequency and phase constant

## Slide 22
Advantages and disadvantages of AM
Amplitude Modulation is easier to implement.
The components used in building the AM transmitter and AM receiver are very cheap.
It can be demodulated using a circuit consisting of very few components.
Poor Performance due to noise.
Inefficient use of transmitter power.
It is not efficient in terms of its use of bandwidth, requiring a bandwidth equal to twice that of the highest frequency.
Advantages of Amplitude Modulation
Disadvantages of Amplitude Modulation
Applications of Amplitude Modulation
Broadcast Transmissions
Air-band radio
Single sideband
Quadrature Amplitude Modulation

## Slide 23
Frequency Modulation
Frequency modulation is the process by which the frequency of a carrier signal changes with respect to the modulating signal.
The total bandwidth required for FM can be determined from the bandwidth of the audio signal: BFM = 2(1 + β)B. Where β is a factor depends on modulation technique with a common value 4.

## Slide 24
Advantages and disadvantages of FM
The amplitude of the frequency-modulated wave does not get affected.
Large decrease in noise, hence increase in the signal to noise ratio.
Noise may reduce by increasing the frequency deviation.
Frequency allocation allows for a guard band which reduces adjacent channel interference.
It operates in a very high frequency called VHF.
FM cannot cover large areas.
Transmitting and receiving equipment of frequency modulation is complex and expensive.
A much wider channel typically 200 kHz is required by FM..
The antennas for FM need to be closely placed for better signals.
Advantages of Frequency Modulation
Disadvantages of Frequency Modulation
Applications of Frequency Modulation
Telemetry, radar and seismic prospecting, EEG monitoring
It is used in radio broadcasts
It is used for audio frequency synthesis.

## Slide 25
Phase Modulation
In PM the instantaneous change in the carrier frequency is proportional to the derivative of the amplitude of the modulating signal. The total bandwidth required for PM can be determined from the bandwidth and maximum amplitude of the modulating signal: BPM = 2(1 + β)B. The value of β is lower in the case of PM.
In PM transmission, the phase of the carrier signal is modulated to follow the changing voltage level (amplitude) of the modulating signal. The peak amplitude and frequency of the carrier signal remain constant, but as the amplitude of the information signal changes, the phase of the carrier changes correspondingly.

## Slide 26
Advantages and disadvantages of Phase Modulation
Phase modulation (PM) is a simple contrasted to Frequency modulation (FM)
It has a higher transmitter efficiency.
It has a higher noise immunity.
The system cost is quite expensive
Phase ambiguity comes if we exceed its modulation index pi radian(180 degree).
we need frequency multiplier to increase phase modulation index.
Advantages of Phase Modulation
Disadvantages of Phase Modulation
Applications of Phase Modulation
widely used in the transmission of radio waves satellite transmission system
Used in digital synthesizers for generating waveform and signal
Wireless technologies such as GSM, Satellite television, and Wi-Fi.

## Slide 27
Comparison of AM and FM
Amplitude Modulation | Frequency Modulation
In amplitude modulation, the frequency and phase remain the same | In frequency modulation amplitude and phase remain the same
Its modulation index varies from 0 to 1 | Its modulation index is always greater than one
It has only two sidebands | It has an infinite number of sidebands
It has simple circuit | It has complex circuit
The amplitude of the carrier wave is modified in order to send the data or information | The frequency of the carrier wave is modified in order to send the data or information
It requires low bandwidth in the range of 10 kHz | It requires high bandwidth in the range of 200 kHz
In AM received signal is of low quality | In FM received signal is of high quality
It operates in the medium frequency (MF) and high frequency (HF) | It operates in the very high frequency
It has poor sound quality | It has better sound quality

## Slide 28
Digital-to-Analog Conversion

## Slide 29
Digital-to-Analog conversion
Digital-to-Analog conversion is the process of changing one of the characteristics of an analog signal based on the information in digital data

## Slide 30
Types of digital-to-analog conversion
In amplitude shift keying (ASK), amplitude of a carrier is changed using the digital data.
In Frequency shift keying (FSK), the frequency of a carrier is changed using the digital data.
In phase shift keying (PSK), the phase of a carrier signal is changed to represent digital data.
In quadrature amplitude modulation (QAM), both amplitude and phase of a carrier signal are changed to represent digital data

## Slide 31
Data Rate (Bit Rate-N) and Signal Rate (Baud Rate-r)
Data Rate (Bit rate): is the transmission of a number of bits per second.
Signal Rate (Baud rate) is the transmission of number of signal units per second.
In the analog transmission of digital data: the baud rate is less than or equal to the bit rate
The relationship between data rate and baud rate is given by formula: S= N * (1/r) baud
Where N is the data rate (bps) and r is the number of data elements carried in one signal element. The value of r in analog transmission is r=log2L, where L is type of signal element

## Slide 32
Difference between: Data Rate and Signal Rate
Bit Rate | Baud Rate
The number of bits per second is known as the bit rate. | The number of signal units per second is known as the baud rate.
Bit rate determines the number of bits travelled per second. | Baud Rate determines the number of times a signal's status changes.
Bit rate= baud rate x the count of bits per signal unit. | Baud rate= bit rate/ the number of bits per signal unit.
The focus is on computer efficiency. | On the other hand, data transmission over the channel is more concerned.
Bit Rate cannot determine the bandwidth. | It can determine the amount of bandwidth necessary to send the signal.

## Slide 33
Example 3
An analog signal carries 4 bits per signal element. If 1000 signal elements are sent per second, find the bit rate.
Solution
In this case, r = 4, S = 1000 (signal rate, or baud), and N (the bit rate) is unknown. We can find the value of N from

## Slide 34
Example 4
An analog signal has a bit rate of 8000 bps and a baud rate of 1000 baud. How many data elements are carried by each signal element? How many signal elements do we need?
Solution
In this example, S = 1000 baud, N = 8000bps, and r and L are unknown. We find first the value of r and then the value of L.

## Slide 35
Amplitude Shift Keying (ASK)
In amplitude shift keying, the amplitude of the carrier signal is varied to create signal elements. Both frequency and phase remain constant while the amplitude changes.
ASK is normally implemented using only two levels. This is referred to as binary amplitude shift keying or on-off keying (OOK). The peak amplitude of one signal level is 0; the other is the same as the amplitude of the carrier frequency

## Slide 36
Bandwidth of Amplitude Shift Keying (ASK)
Carrier signal is only sine wave, the process of modulation produces a non periodic composite signal.
Bandwidth is proportional to signal rate(baud rate).
There is another factor involved called as d, which depends on modulation and filtering process. The value of d is between 0 and 1.
Bandwidth can be expressed as shown
B= (1+d) * S
Where B is the bandwidth and S is the signal rate.
The middle of bandwidth is fc where carrier frequency is located.

## Slide 37
Example 5
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate (N) if we modulated our data by using ASK with d = 1?
Solution
The middle of the bandwidth is located at 250 kHz. This means that our carrier frequency can be at fc = 250 kHz. We can use the formula for bandwidth to find the bit rate (with d = 1 and r = 1).
Bandwidth = (1+d) * baud rate S
Don’t want to know baud rate S, we want to know bit rate N, so substitute S = N * 1/r
Bandwidth = (1+d) * N * 1/r
100kHz = 2 N * 1/1 (given r=1 and d=1)
100kHz = 2N
N = 50 kbps

## Slide 38
Amplitude Shift Keying (ASK)
Advantages
It can be used to transmit digital data over optical fiber.
The receiver and transmitter have a simple design which also makes it comparatively inexpensive.
It uses lesser bandwidth as compared to FSK thus it offers high bandwidth efficiency.
Disadvantages
It is susceptible to noise interference and entire transmissions could be lost due to this.
It has lower power efficiency
ASK techniques are not suitable for high bit rate data transmission
Applications
Home automation devices.
Industrial networks devices.
Wireless base stations.

## Slide 39
Frequency Shift Keying (FSK)
In frequency shift keying, the frequency of the carrier signal is varied to represent
data. The frequency of the modulated signal is constant for the duration of one signal element, but changes for the next signal element if the data element changes. Both amplitude and phase remain constant for all signal elements.
Carrier signal are simple sine waves, but modulation creates a non periodic composite signal with continuous frequencies. We can say that FSK as two ASK signal with its own carrier frequencies (f1 or f2). The Difference between two frequencies is 2Df then the required bandwidth is B= (1+d)*S + 2Df

## Slide 40
Frequency Shift Keying (FSK)
Advantages
The antenna size reduced.
Avoid multiplexing of signals, decrease the SNR.
Long-range communication can be possible.
Disadvantages
It uses larger bandwidth compare to ASK and PSK. Hence it is not bandwidth efficient.
The bit error rate is less in AEGN channel than phase shift keying.

## Slide 41
Phase Shift Keying (PSK)
In phase shift keying, the phase of the carrier is varied to represent two or more different signal elements. Both peak amplitude and frequency remain constant as the phase changes.
d = 0 for PSK
Bandwidth is same as that for binary ASK, but less than that for Binary FSK (BFSK). No Bandwidth is wasted for separating two carrier signal

## Slide 42
Phase Shift Keying (PSK)
Binary PSK is as simple as binary ASK with one big advantage-it is less susceptible to noise. In ASK, the criterion for bit detection is the amplitude of the signal; in PSK, it is the phase.
Noise can change the amplitude easier than it can change the phase.
In other words, PSK is less susceptible to noise than ASK. PSK is superior to FSK because we do not need two carrier signals.
Advantages
It is more power efficient modulation technique compare to ASK and FSK.
Disadvantages
It has lower bandwidth efficiency.

## Slide 43: Quadrature Amplitude Modulation (QAM)
Quadrature amplitude modulation is a combination of ASK and PSK.
QAM uses two carriers, one in-phase and the other quadrature, with different amplitude levels for each carrier.
Bandwidth for QAM
The minimum bandwidth required for QAM transmission is the same as that required for ASK and PSK transmission. QAM has the same advantages as PSK over ASK.
Advantages
Efficient usage of bandwidth.
Disadvantages
QAM modulation is more susceptible to the noise
Linear amplifier is needed which consumes more power
Applications
Used in the radio communications
Used in optical fiber systems to increase bit rates

## Slide 44
Digital-to-Digital Conversion
Line coding
Block coding
Scrambling

## Slide 45
Digital-to-Digital conversion
Digital-to-digital conversion techniques, methods which convert digital data to digital signals.
The conversion involves Three techniques:
  Line Coding
  Block Coding
  Scrambling
Note: Line coding is always needed; block coding and scrambling may or may not be needed.

## Slide 46
Line Coding
Line coding is the process of converting digital data to digital signals.
At the sender, digital data are encoded into a digital signal; at the receiver, the digital data are recreated by decoding the digital signal.
High voltage level (+V) could represent a “1” and a low voltage level (0 or -V) could represent a “0”.

## Slide 47
Line Coding
We define a ratio r which is the number of data elements carried by each signal element.
In part a: of the figure, one data element is carried by one signal element (r = 1).
In Part b: we need two signal elements (two transitions) to carry each data element (r = 1/2 ).
In part c: a signal element carries two data elements (r = 2).
In part d: a group of 4 bits is being carried by a group of three signal elements (r =4/3).

## Slide 48
Data Rate Versus Signal Rate
The data rate defines the number of data elements (bits) sent in 1s.
The unit is bits per second (bps).
The signal rate is the number of signal elements sent in 1s. The unit is the baud.
There are several common terminologies used in the literature.
The data rate is sometimes called the bit rate; the signal rate is sometimes called the pulse rate, the modulation rate, or the baud rate.
One goal: To increase the data rate while decreasing the signal rate.
Increasing the data rate increases the speed of transmission; decreasing the signal rate decreases the bandwidth requirement.

## Slide 49
Line Coding Characteristics
1. Data Rate versus Signal Rate:
The data rate defines the number of data elements (bits) sent in 1s. The unit is bits per second (bps). The data rate is sometimes called the bit rate
The signal rate is the number of signal elements sent in 1s. The unit is the baud. The signal rate is sometimes called the pulse rate, the modulation rate, or the baud rate.
Goal in data communications is to increase the data rate while decreasing the signal rate.
      Increasing the data rate increases the speed of transmission.
      Decreasing the signal rate decreases the bandwidth requirement.

## Slide 50
Line Coding Characteristics
2. Bandwidth:
Digital signal that carries information is non-periodic.
The bandwidth of a non-periodic signal is continuous with an infinite range.
However, most digital signals we encounter in real life have a bandwidth with finite values.
The bandwidth is theoretically infinite, but many of the components have such a small amplitude that they can be ignored.
The effective bandwidth is finite.

## Slide 51
Line Coding Characteristics
3. Baseline Wandering: In decoding a digital signal, the receiver calculates a running average of the received signal power. This average is called the baseline.
The incoming signal power is evaluated against this baseline to determine the value of the data element.
A long string of 0 s or 1s can cause a drift in the baseline (baseline wandering) and make it difficult for the receiver to decode correctly.
A good line coding scheme needs to prevent baseline wandering.

## Slide 52
Line Coding Characteristics
5. DC Components:
When the voltage level in a digital signal is constant for a while, the spectrum creates very low frequencies
These frequencies around zero, called DC (direct-current) components
This DC component present problems for a system that cannot pass low frequencies or a system that uses electrical coupling (via a transformer).

## Slide 53
Line Coding Characteristics
6. Self-synchronization:
To correctly interpret the signals received from the sender, the receiver's bit intervals must correspond exactly to the sender's bit intervals.
If the receiver clock is faster or slower, the bit intervals are not matched and the receiver might misinterpret the signals.
The following figure represents the synchronization problem.

## Slide 54
Line Coding Characteristics
7. Built-in Error Detection:
It is desirable to have a built-in error-detecting capability in the generated code to detect some of or all the errors that occurred during transmission.
8. Immunity to Noise and Interference:
Another desirable code characteristic is a code that is immune to noise and other interferences.
9. Complexity:
A complex scheme is more costly to implement than a simple one.
For example, a scheme that uses four signal levels is more difficult to interpret than one that uses only two levels.

## Slide 55
Example 6
A signal is carrying data in which one data element is encoded as one signal element ( r = 1). If the bit rate is 100 kbps, what is the average value of the baud rate if c is between 0 and 1? Assume that the average value of c is 1/2
c is the case factor (worst, best & avg.) =1/2
S = c x N x 1/r bauds
N is data rate =100 kbps=100,000
r is the ratio between data element & signal element = 1/1

## Slide 56
Line Coding Schemes
And RZ

## Slide 57
1. Unipolar NRZ scheme
In a unipolar scheme, all the signal levels are on one side of the time axis, either above or below. In Non-Return-to-Zero, the signal does not return to zero at the middle of the bit, where positive voltage defines bit 1 and the zero voltage defines bit 0.
It is simple but costly in power consumption.
Sequence of bits=10110
Advantages
It is simple.
A lesser bandwidth is required.
Disadvantages
No error correction done.
Presence of low frequency components may cause the signal droop.
Loss of synchronization is likely to occur (especially for long strings of 1s and 0s).

## Slide 58
1.Unipolar Return to Zero
Advantages
It is simple.
The spectral line present at the symbol rate can be used as a clock.
Disadvantages
The disadvantages of Unipolar RZ are −
No error correction.
Occupies twice the bandwidth as unipolar NRZ.
The signal droop is caused at the places where signal is non-zero at 0 Hz

## Slide 59
2. Polar NRZ scheme
a. Non-Return-to-Zero (NRZ):
The voltages are on both sides of the time axis.
Polar NRZ scheme can be implemented with two voltages. E.g. -V for 1 and +V for 0.
There are two versions:
    1. NZR - Level (NRZ-L) - positive voltage for zero symbol and negative for the other.
    2. NRZ - Inversion (NRZ-I) - the change or lack of change in polarity determines the value of a symbol. E.g. a “1” symbol inverts the polarity a “0” does not.
Advantages
It is simple.
No low-frequency components are present.
Disadvantages
No error correction.
No clock is present.
The signal droop is caused at the places where the signal is non-zero at 0 Hz.

## Slide 60
2.Polar RZ scheme
b. Return-to-Zero (RZ):
This scheme uses three voltage values. +, 0, -.
Each symbol has a transition in the middle. Either from high to zero or from low to zero.
Advantages
It is simple.
No low-frequency components are present.
Disadvantages
No error correction.
No clock is present.
Occupies twice the bandwidth of Polar NRZ.
The signal droop is caused at places where the signal is non-zero at 0 Hz.

## Slide 61
2. Polar Schemes : Manchester

## Slide 62
2. Polar Schemes : Manchester

## Slide 63
2. Polar Schemes : Differential Manchester

## Slide 64
2. Polar Schemes : Differential Manchester cont-

## Slide 65
2. Polar Schemes : Differential Manchester
In Manchester and differential Manchester encoding, the transition at the middle of the bit is used for synchronization
The minimum bandwidth of Manchester and differential Manchester is 2 times that of NRZ.

## Slide 66
3. Bipolar: Alternate Mark Inversion (AMI) and Pseudoternary (only for student Information)
Alternate Mark Inversion (AMI) and Pseudoternary.
Mark means 1. So AMI means alternate 1 inversion.
A neutral zero voltage represents binary 0. Binary 1s are represented by alternating positive and negative voltages.
A variation of AMI encoding is called Pseudoternary in which the 1 bit is encoded as a zero voltage and the 0 bit is encoded as alternating positive and negative voltages.
AMI is commonly used for long-distance communication, but it has a synchronization problem when a long sequence of O’s (Zero) is present in the data.

## Slide 67
Bipolar
Advantages
It is simple.
No low-frequency components are present.
Occupies low bandwidth than unipolar and polar NRZ schemes.
This technique is suitable for transmission over AC coupled lines, as signal drooping doesn’t occur here.
A single error detection capability is present in this.
Disadvantages
No clock is present.
Long strings of data causes loss of synchronization.

## Slide 68
Summary of line coding schemes PN 151

## Slide 69: 2. Block Coding
A technique of sending data in a set of sequence.
Block coding is done in three steps:
  1. Division
  2. Substitution
  3. Combination.
Need to add redundant bits for padding, error checking
https://www.youtube.com/watch?v=l-C_st2Oq0A
We need redundancy (extra bits) bits are required during transmission: to ensure synchronization and to provide some kind of inherent error detecting.
Block coding can give us this redundancy and improve the performance of line coding.
Block coding is also called as mB/nB coding (m Bits, n Bits).
Changing Block of m Bits to Block of n Bits. Where n>m.

## Slide 70: Block Coding
  Division
  divide a sequence of bits into groups of m bits each)
  2. Substitution (replace m-bit group with an n-bit group.)
  3. Combination (n-bit groups are combined together to form a stream and this steam has more bits of data than original bits)

## Slide 71: Scrambling
The scrambling does not increase or decrease the bit rate i.e. the input and output bits are same in size.
It helps in synchronization as long string of 0s and 1s are removed from the digital data which creates more level transitions in the data pattern.
There are two common scrambling techniques:
B8ZS(Bipolar with 8-zero substitution)
HDB3(High-Density Bipolar3-zero)
B8ZS (Bipolar with 8-zero substitution): This technique is similar to Bipolar AMI except when eight consecutive zero-level voltages are encountered they are replaced by the sequence, “000VB0VB”. V-Violation and B-Bipolar

## Slide 72: Scrambling
Earlier coding schemes are not suitable for long distance because of DC component.
Scrambling means rearranging data sequence.
Ex. 01101100 changed to 01010110
Significance: It prevents unauthorized access to data
Significance: Timing Extraction---- to avoid long sequence of 0’s or1’s.
Scrambling is a technique to avoid long sequence of 0’s used to create a sequence of bits that has the required for transmission - self clocking, no low frequencies, no wide bandwidth.

## Slide 73: Scrambling
a.
Previous voltage level is Positive
https://www.youtube.com/watch?v=DtfUPa7RG9s
The V in the sequence denotes violation, this is a nonzero voltage that breaks an AMI rule of encoding (opposite polarity from the previous).
The B in the sequence denotes bipolar, which means a nonzero level voltage in accordance with the AMI rule.

## Slide 74: Scrambling
a.
Previous voltage level is Negative
cont-

## Slide 75: Scrambling cont-
b.
High-Density Bipolar 3 -zero

## Slide 76: Scrambling cont-
HDB3 (High-density bipolar3-zero): In this technique, four consecutive zero-level voltages are replaced with a sequence “000V” or “B00V”.
Rules for using these sequences:
If the number of nonzero pulses after the last substitution is odd, the substitution pattern will be “000V”, this helps in maintaining a total number of nonzero pulses even.
If the number of nonzero pulses after the last substitution is even, the substitution pattern will be “B00V”. Hence even the number of nonzero pulses is maintained again.

## Slide 77
Data Rate (Bit Rate) and Signal Rate (Baud Rate)
Bit rate (data rate) is the number of bits per second.
Baud rate (signal rate) is the number of signal elements per second.
In the analog transmission of digital data, the baud rate is less than or equal to the bit rate
The relationship between data rate and baud rate is given by following formula
S= N * (1/r) baud
Where N is the data rate (bps) and r is the number of data elements carried in one signal element.
The value of r in analog transmission is r=log2L, where L is type of signal element

## Slide 78: Analog-to-Digital Conversion
Two techniques
  Pulse Code Modulation (PCM)
  Delta Modulation (DM)

## Slide 79
Analog-to-Digital Conversion
A digital signal is superior to an analog signal.
It is more robust to noise and can easily be recovered, corrected and amplified. For this reason, it is better to change an analog signal to digital data.
Analog-to-Digital Conversion: Two techniques
  Pulse Code Modulation (PCM)
  Delta Modulation (DM)—only for self study

## Slide 80
Components of PCM encoder
Pulse Code Modulation.
Analog to digital conversion. Digitization.
1. The analog signal is sampled. 2. The sampled signal is quantized. 3. The quantized values are encoded as streams of bits.
Pulse Amplitude Modulation
Encoder

## Slide 81
PCM
Advantages
Disadvantages
Applications

## Slide 82
Delta Modulator (Only for student’s information)
PCM is a very complex technique. Other techniques have been developed to reduce the complexity of PCM.
The simplest is delta modulation.
PCM finds the value of the signal amplitude for each sample; DM finds the change from the previous sample.
Note that there are no code words here; bits are sent one after another.
Figure The process of delta modulation

## Slide 83
Delta Modulation Components (Only for student’s information)
Modulator: is used at the sender site to create a stream of bits from an analog signal.
If the delta is positive, the process records a 1; if it is negative, the process records a 0.
Base of comparison is required. Which is done by Staircase Maker.
The modulator, at each sampling interval, compares the value of the analog signal with the last value of the staircase signal.
Note that we need a delay unit to hold the staircase function for a period between two comparisons.

## Slide 84
Delta Demodulation Components (Only for student’s information)
Demodulator: The demodulator takes the digital data and, using the staircase maker and the delay unit, creates the analog signal.
Low-pass filter is used for smoothing.
Adaptive DM: A better performance can be achieved if the value of δ is not fixed. In adaptive delta modulation, the value of δ changes according to the amplitude of the analog signal.
Quantization Error: DM is not perfect. Quantization error is always introduced in the process. The quantization error of DM, however, is much less than that for PCM.

## Slide 85: Types of Networks 1: Personal Area Networks (PAN) 2: Local Area Networks (LAN) 3: Metropolitan Area Networks (MAN) 4: Wide Area Networks (WAN) 5: Ad-Hoc Network
https://www.youtube.com/watch?v=vrh0epPAC5w&list=PL1kr2FHR_uFHQk2hy2g8lr7ouBhSJFEk_&index=1

## Slide 86
Computer Networks
Autonomous computers are network or a collection of networks that are all managed and supervised by a single entity or organization
Two or more autonomous computers are connected.
Geographic location: anywhere

## Slide 87
Types of Networks
Classification of interconnected processors:
Personal area networks (PAN)
Local area networks (LAN)
Metropolitan area networks (MAN)
Wide area networks (WAN)
Ad-Hoc Network

## Slide 88
1. Personal Area Network (PAN)

## Slide 89
2. Local Area Network (LAN)
Wireless and Wired LAN
(a) 802.11 (b) Switched Ethernet
(a) 802.11 (standard which defines protocols for Wireless Local Area Networks)
(b) Switched Ethernet (Ethernet provides services for wired media)

## Slide 90
3. Metropolitan Area Network (MAN):
based on cable TV

## Slide 91
4. Wide Area Network (WAN)
WAN: connects three branch offices in Australia

## Slide 92
5. Ad-hoc Network
"Ad Hoc" is a Latin phrase that means "for this purpose."
An ad hoc network is a temporary network created between two devices without utilizing any other networking infrastructure. These networks exist for a single session, often for a specific purpose like transferring files or sharing an Internet connection. Ad hoc networks do not require a router or wireless access point.

## Slide 93
Comparison of LAN, MAN, WAN
Sr.No. | Key | LAN | MAN | WAN
1 | Definition | LAN stands for Local Area Network. | MAN stands for Metropolitan Area Network. | WAN stands for Wide Area Network.
2 | Ownership | LAN is often owned by private organizations. | MAN ownership can be private or public. | WAN ownership can be private or public.
3 | Speed | LAN speed is quiet high. | MAN speed is average. | WAN speed is lower than that of LAN.
4 | Delay | Network Propagation Delay is short in LAN. | Network Propagation Delay is moderate in MAN. | Network Propagation Delay is longer in WAN.
5 | Congestion | LAN has low congestion as compared to WAN. | MAN has higher congestion than LAN. | WAN has higher congestion than both MAN and LAN.
6 | Fault Tolerance | Fault Tolerance of LAN is higher than WAN. | Fault Tolerance of MAN is lower than LAN. | Fault Tolerance of WAN is lower than both LAN and MAN.
7 | Maintenance | Designing and maintaining LAN is easy and less costly than WAN. | Designing and maintaining WAN is complex and more costly than LAN. | Designing and maintaining WAN is complex and more costly than both LAN and MAN.

## Slide 94
Uses of Computer Networks
Business Applications
Home Applications: P2P having no fixed clients & servers

## Slide 95: Uses of Computer Networks
Mobile Users: Combinations of wireless networks and mobile computing
Social Issues
    Network neutrality
    Digital Millennium Copyright Act
    Profiling users
    Phishing

## Slide 96
Network Architectures
  Client-Server
  Peer-to-Peer
  Distributed Network
  Software Define Network

## Slide 97
1. Client-Server Model
Client-server model: involves Requests and Replies

## Slide 98
2. Peer-to-Peer Architecture
All nodes acts as a clients and servers
  - Provides and consume data
  - Any node can initiate a connection
No centralized data source
  -The ultimate form of democracy on the Internet
  -The ultimate threat to copy-right protection on
  the Internet

## Slide 99
3. Distributed Network
Distributed networks are part of distributed computing architecture, in which enterprise IT infrastructure resources are divided over a number of networks, processors and intermediary devices

## Slide 100
4. Software Define Network
Software-Defined Networking (SDN) is dynamic, manageable, cost-effective, and adaptable for the high-bandwidth, dynamic nature of today’s applications.
This architecture decouples the network control and forwarding functions enabling the network control to become directly programmable and the underlying infrastructure to be abstracted for applications and network services.

## Slide 101: Network Topologies: 1. Bus Topology 2. Star Topology 3. Extended star or Tree Topology 4. Ring Topology 5. Mesh Topology

## Slide 102
Network Topologies
Way of connection between computers, printers and other devices.
Layout of the wire and devices as well as the paths used by data transmissions.

## Slide 103
Bus Topology
Commonly referred as a linear bus
All the devices are connected by one single cable
Advantages
It is easy to set up, handle, and implement.
It is best-suited for small networks.
It costs very less.
Disadvantages
The cable length is limited - limits the number of network nodes
When the number of devices connected to the bus increases, the efficiency decreases.
A fault in the central bus leads to network failure.
Each device on the network “sees” all the data being transmitted.

## Slide 104
Star Topology
Star topology
most commonly used architecture in Ethernet LANs
resembles spokes in a bicycle wheel
Advantages of Star Topology
Due to its centralized nature, the topology offers simplicity of operation.
It also achieves isolation of each device in the network.
Adding or removing network nodes is easy.
Due to the centralized nature, it is easy to detect faults in the network devices.
Disadvantages of Star Topology
Network operation depends on the functioning of the central hub. Hence, central hub failure leads to failure of the entire network.
Also, the number of nodes that can be added, depends on the capacity of the central hub.
The setup cost is quite high.

## Slide 105
Tree Topology
Extended star topology or tree topology
significantly reduces the traffic on the wires by sending packets only to the wires of the destination host
network devices that filter frames or packets like bridges, switches and routers
Advantages of Tree Topology
The tree topology is useful in cases where a star or bus cannot be implemented individually.
Fault identification is easy.
The network can be expanded by the addition of secondary nodes. Thus, scalability is achieved.
Disadvantages of Tree Topology
As multiple segments are connected to a central bus, the network depends heavily on the bus. Its failure affects the entire network
Owing to its size and complexity, maintenance is not easy and costs are high
Though it is scalable, the number of nodes that can be added depends on the capacity of the central bus and on the cable type.

## Slide 106
Ring Topology
A frame travels around the ring, stopping at each node
A Node wants to transmit data it adds the data as well as the destination address to the frame, which takes the data out of the frame
Single ring – all the devices on the network share a single cable
Dual ring – allows data to be sent in both directions
Advantages of Ring Topology
A central server is not required
The traffic is unidirectional and the data transmission is high-speed
In comparison to a bus, a ring is better at handling load.
The adding or removing of network nodes is easy.
It is less costly than a star topology.
Disadvantages of Ring Topology
The failure of a single node in the network can cause the entire network to fail
The movement made to network nodes affect the entire network’s performance.

## Slide 107
Mesh Topology
Connects all devices (nodes) to each other for redundancy and fault tolerance
Used in WANs to interconnect LANs and for mission critical networks like those used by banks and financial institutions
Implementation is Expensive and difficult
Advantages of Mesh Topology
Possible to transmit data from one node to many other nodes at the same time.
The failure of a single node does not cause the entire network to fail
It can handle heavy traffic
Easy to identify faults.
Disadvantages of Mesh Topology
A lot of cabling is required.
Costly setup and maintenance
Administration of a mesh network is difficult

## Slide 108
Comparison of network Topologies
Topology | Information Transfer | Setup | Expansion | Troubleshooting | Cost | Cabling Concerns
Star Each computer connects to a central connection device. | All information passes through the central network connection. | Each computer must be close to the central device. 100 meters maximum cable length. Up to 24 computers per network. | Add a new computer by plugging in a new cable from the computer to the connection device. | When one computer goes down, the rest of the network is unaffected. If the connection device goes down, then the network is down. | More expensive of the simple topologies, it requires costly connection device. Usually cheaper than a hybrid network. | Uses twisted pair cable. Requires large amounts of cable. No more than 100 meters from the computer to the connection device.
Bus Single cable connects everything. | One computer at a time sends information. Information goes along the cable and the computer accesses the information off the cable. | Connect the cable from one computer to the next and so on to the end. A terminator is placed at each end of the network. | To add a computer, you must shut down the network and disconnect the cable from the existing computers. | If one computer malfunctions, the entire network goes down. | A cheaper network since there is usually one continuous copper cable. | Single continuous cable connects the devices. Terminator is required at each end of the cable. Uses coaxial or twisted pair cabling.

## Slide 109
Comparison of network Topologies cont-
Ring Single cable configured in a ring. | Information goes in one direction around the ring and passes along the ring until it reaches the correct computer. | Computers are located close to each other. Setup is easy. There is no connector. The ring has no beginning and no end. | Cable between the computers must be broken to add a new computer, so the network is down until the new device is back online. | If there's a break in the cable or an error in the network, information continues to transfer through the rest of the ring until reaching the point of the break. This makes troubleshooting easy. | One of the more expensive topologies due to high cable costs. | Requires more cabling than other topologies. Uses twisted pair.
Hybrid Mesh Combines two or more different structures. | Often used across long distances. Information transfer can happen in different ways, depending on the other topologies. | Often created when expanding an existing network. Can use a variety of connection devices. | Connection devices make combining different networks and different topologies easy. | Troubleshooting is most difficult in this topology because of the variety of technologies. | Expensive, large, and usually complicated. | Cabling depends on the types of networks. Can use twisted pair and coaxial cable. Also incorporates fiber optic cabling over long distances.

## Slide 110: Transmission Media’s

## Slide 111
Transmission Media
Transmission medium and physical layer
Transmission media is a communication channel that carries the information from the sender to the receiver.
Transmission media is of two types are wired media and wireless media.
Different transmission media have different properties such as bandwidth, delay, cost and ease of installation and maintenance.
Transmission media are located below the physical layer

## Slide 112
Classification of Transmission Media

## Slide 113
Twisted-Pair Cable
A twisted pair consists of two conductors basically copper based with its own plastic insulation, twisted together.
One of the wires is used to carry signals to the receiver, and the other is used only as a ground reference. The receiver uses the difference between the two.

## Slide 114
Twisted-Pair Cable
UTP cable
STP cable
The most common twisted-pair cable used in communications is referred to as unshielded twisted-pair (UTP). IBM has also produced a version of twisted-pair cable for its use called shielded twisted-pair (STP). STP cable has a metal foil or braided mesh covering that encases each pair of insulated conductors. Although metal casing improves the quality of cable by preventing the penetration of noise or crosstalk, it is bulkier and more expensive.
(unshielded twisted-pair)
(shielded twisted-pair)

## Slide 115
Twisted-Pair Cable
UTP cable
STP cable
Advantages of Unshielded Twisted Pair:
It is cheap.
Installation of the unshielded twisted pair is easy.
It can be used for high-speed LAN.
Disadvantage:
This cable can only be used for shorter distances because of attenuation..
Advantages of Shielded Twisted Pair:
An installation of STP is easy.
It has higher capacity as compared to unshielded twisted pair cable.
It is shielded that provides the higher data transmission rate.
Disadvantages
It is more expensive as compared to UTP
It has a higher attenuation rate.

## Slide 116
Twisted-pair cable

## Slide 117
Coaxial Cable
Coaxial cable (Coax) is very commonly used for example, TV wire is usually a coaxial cable.
Coaxial - contains two conductors parallel to each other.
It has a higher frequency as compared to Twisted pair cable.
The inner conductor of the coaxial cable is made up of copper, and the outer conductor is made up of copper mesh.
Advantages Of Coaxial cable:
The data can be transmitted at high speed.
It has better shielding as compared to twisted pair cable.
It provides higher bandwidth.
Disadvantages of Coaxial cable:
It is more expensive as compared to twisted pair cable.
If any fault occurs in the cable causes the failure in the entire network.
Applications
was widely used in analog telephone networks
Cable TV networks
Can carry 10,000 voice signals.
Traditional Ethernet LANs

## Slide 118
Fiber-Optic Cable
Fiber optic cable is a cable that uses light signals for communication.
Fiber optic is a cable that holds the optical fibers coated in plastic that are used to send the data by pulses of light.
The plastic coating protects the optical fibers from heat, cold, electromagnetic interference from other types of wiring.
Fiber optics provide faster data transmission than copper wires.

## Slide 119
Fiber-Optic Cable
Advantages of Fiber-optic cable
Higher bandwidth: The fiber optic cable provides more bandwidth as compared copper.
Fiber optic cable carries the data in the form of light. This allows the fibre optic cable to carry the signals at a higher speed.
Less signal attenuation: Fiber-optic transmission distance is significantly greater than that of other guided media.
Immunity to electromagnetic interference: Electromagnetic noise cannot affect fiber-optic cables.
Resistance to corrosive materials: Glass is more resistant to corrosive materials than copper.
Light weight: Fiber-optic cables are much lighter than copper cables.
Greater immunity to tapping: Fiber-optic cables are more immune to tapping than copper cables.
Disadvantages of Fiber-optic cable
Installation and maintenance: Its installation and maintenance require expertise that is not yet available everywhere.
Unidirectional light propagation: Propagation of light is unidirectional.
Cost: The cable and the interfaces are relatively more expensive than those of other guided media.

## Slide 120
UNGUIDED MEDIA: WIRELESS
An unguided transmission transmits the electromagnetic waves without using any physical medium. Therefore it is also known as wireless transmission.
The electromagnetic spectrum, ranges from 3 kHz to 900 kHz, used for wireless communication.

## Slide 121
UNGUIDED MEDIA: WIRELESS
Radio Waves
Electromagnetic waves ranging in frequencies between 3Khz to 1 GHz are called radio waves
Radio waves are omnidirectional, i.e., the signals are propagated in all the directions.
Applications of Radio waves:
Radio waves are used for multicast communications, such as radio and television, and paging systems.

## Slide 122
UNGUIDED MEDIA: WIRELESS
Microwaves
Electromagnetic waves having frequencies between 1GHz and 300 GHz are called microwaves.
Microwaves are unidirectional. When an antenna transmits microwave waves, they can be narrowly focused. This means that the sending and receiving antennas need to be aligned.
The unidirectional property has an obvious advantage. A pair of antennas can be aligned without interfering with another pair of aligned antennas.
Applications:
Microwaves are used for unicast communication such as cellular telephones, satellite networks, and wireless LANs

## Slide 123
Infrared
Frequencies from 300 GHz to 400 THz
Used for short-range communication
Applications:
Infrared waves are used for short-range communications such as those between a PC and a peripheral device.
TV remote operation
They can also be used for indoor LANs.

## Slide 124: Networking Devices

## Slide 125
Layer wise Networking Devices
(a) Layer wise devices (b) Frames, packets and headers
Cyclic Redundancy Check

## Slide 126
Networking Devices
Networking devices are Repeaters, Hubs, Bridges, Switches, Routers and Gateways.
Repeater
A repeater operates at the Physical layer.
A repeater receives a signal and, before it becomes too weak or corrupted, regenerates the original bit pattern.
A repeater is a regenerator, not an amplifier.
Hub
Hub is used to connect devices to the same network (Physical layer).
Hubs cannot filter data, so data packets are sent to all connected devices

## Slide 127
Networking Devices
Bridge
A bridge operates at data link layer
It is also used for interconnecting two LANs working on the same protocol.
Switch
A switch is a data link layer device
It is an intelligent network device that can be conceived as a multiport network bridge.
It uses MAC addresses to send data packets to selected destination ports
Switches can perform some error checking before forwarding data.
MAC Address: Medium access control: unique 48-bit hardware numbers of a computer that are embedded into a network card (known as a Network Interface Card) during manufacturing. The MAC Address is also known as the Physical Address of a network device. 00:00:0A:BB:28:FC

## Slide 128
Networking Devices
Router
Routers operate at the Network Layer (Layer 3)
Interconnect IP networks
Gateway:
A gateway is simply a device or hardware that acts as a "gate" between the networks.
A gateway is a network node used in telecommunications that connects two networks with different transmission protocols together
The gateway converts information, data or other communications from one protocol or format to another
An Internet gateway can transfer communications between an enterprise network and the Internet
Difference between Gateway and Router
A gateway connects networks, while a router typically delivers data within a network
it's becoming more common for their functions to be combined and simply called a router

## Slide 129
Comparison of network devices
HUB | SWITCH | ROUTER
Hub is a broadcast device. | The switch is a multicast device. | The router is a routing device.
Hub works in the physical layer of OSI model. | The switch works in data link layer. | The router works in the network layer of OSI model.
Hub is used to connect devices to the same network. | The switch is used to connect devices to the network. | The router is used to connect two different networks.
Hub sends data in the form of bits. | The switch sends data in the form of frames. | The router sends data in the form of packets.
Hub works in half duplex. | The switch works in full duplex. | The router works in full duplex.
Only one device can send data at a time. | Multiple devices can send data at a time. | Multiple devices can send data at a time.
Hub does not store any MAC address of a node in the network. | It uses MAC addresses | It uses IP Addresses

## Slide 130: OSI (Open Systems Interconnection ) Reference Model and TCP/IP Model
Data communication is a process or act in which we can send or receive data.
For data communication two models are available.
OSI: It was developed in 1984 by the International Organization for Standardization (ISO).
TCP/IP: It was designed by Vint Cerf and Bob Kahn in the 1970s.

## Slide 131
OSI Model: duties for each layer

## Slide 132
OSI Reference Model
OSI: Open Systems Interconnection
The OSI provides a standard for different computer systems to be able to communicate with each other.
Layers created for different abstractions
Each layer performs well-defined function
Function of layer chosen with definition of international standard protocols in mind
Minimize information flow across interfaces between boundaries.
Number of layers optimum.
The Open Systems Interconnection model (OSI model) is a conceptual model from the International Organization for Standardization (ISO) that "provides a common basis for the coordination of standards development for the purpose of systems interconnection
was funded primarily by the U.S. Department of Defense.

## Slide 133
OSI Reference Model (Extra)
  Application layer
  Presentation layer
  Session layer
  Transport layer
  Network layer
  Data link layer
  Physical layer

## Slide 134
TCP/IP Model
Process to process
(Data)
Host to Host (Segment)
Source to Destination
(Packet)
Node to Node
(Frame)
Fundamental Model (All about TH)
Implementable Model (All about Practical)

## Slide 135
TCP/IP Model
TCP :Transmission Control Protocol, IP : Internet Protocol
The main work of TCP/IP is to transfer the data of a computer from one device to another.
TCP/IP model divides its data into packets and combines them at the other end, which helps in maintaining the accuracy of the data while transferring from one end to another end.
IP finds the destination of the mail and TCP has the work to send and receive the mail.
The Advanced Research Projects Agency Network (ARPANET) was the first wide-area packet-switched network with distributed control and one of the first computer networks to implement the TCP/IP protocol suite.

## Slide 136
TCP/IP Model: Protocols
HTTP:The Hypertext Transfer Protocol
SMTP: Simple mail transfer protocol.
ICMP: Internet Control Message Protocol
UDP: User Datagram Protocol
TCP: Transmission Control Protocol
SONET: Synchronous Optical Network
DSL: Digital Subscriber Line
802.11 and Ethernet: are examples of standard
LAN technologies.
The connection between the devices could be wired or wireless.

## Slide 137
OSI model protocols

## Slide 138
Comparison of OSI & TCP/IP Reference Models
OSI (Open System Interconnection) developed by ISO (International Standard Organization) | TCP/IP(Transmission Control Protocol / Internet Protocol) developed by ARPANET (Advanced Research Project Agency Network).
1. OSI is a generic, protocol independent standard, acting as a communication gateway between the network and end user. | 1. TCP/IP model is based on standard protocols around which the Internet has developed. It is a communication protocol, which allows connection of hosts over a network.
2. In OSI model the transport layer guarantees the delivery of packets. | 2. In TCP/IP model the transport layer does not guarantees delivery of packets. Still the TCP/IP model is more reliable.
3. Follows vertical approach. | 3. Follows horizontal approach.
4. OSI model has a separate Presentation layer and Session layer. | 4. TCP/IP does not have a separate Presentation layer or Session layer.
5. Transport Layer is Connection Oriented. | 5. Transport Layer is both Connection Oriented and Connection less.

## Slide 139
Comparison of OSI & TCP/IP Reference Models
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol / Internet Protocol)
6. Network Layer is both Connection Oriented and Connection less. | 6. Network Layer is Connection less.
7. OSI is a reference model around which the networks are built. Generally it is used as a guidance tool. | 7. TCP/IP model is, in a way implementation of the OSI model.
8. Protocols are hidden in OSI model and are easily replaced as the technology changes. | 8. In TCP/IP replacing protocol is not easy.
9. OSI model has a problem of fitting the protocols into the model. | 9. TCP/IP model does not fit any protocol
10. OSI model defines services, interfaces and protocols very clearly and makes clear distinction between them. It is protocol independent. | 10. In TCP/IP, services, interfaces and protocols are not clearly separated. It is also protocol dependent.
11. It has 7 layers | 11. It has 4 layers

## Slide 140: Ethernet Standards (Only for self study Student)

## Slide 141
Features | Baseband Transmission | Broadband Transmission
Definition | It is a data transmission technique in which one signal needs the whole bandwidth of the channel to transfer the data. | It is a transmission technology in which many signals with different frequencies send data across a single channel at the same time.
Signal Type | It utilizes digital signals. | It utilizes analog signals.
Topology | It operates with bus topology. | It operates with both bus and tree topology.
Number of Channels | It utilizes the same channel for sending and receiving data. | It utilizes two channels, one for transmission and the second for data reception.
Distance Covered | Signals are only capable of travelling limited distances. | Signals may be transmitted across long distances without attenuation.
Installation | It is simple and easy to install and maintain. | It is complex to install and maintain.
Cost | It is less expensive to design. | It is costly to design.
Encoding Technique | Manchester and differential Manchester encoding are used in baseband. | It utilizes the PSK (Phase shift keying) encoding.
Transfer medium | It utilizes coaxial cables, wires, and twisted-pair cables as the transfer medium for digital signals. | It sends digital signals via coaxial cable, optical fibre cables, and radio waves.
Application | It is usually found in Ethernet. | It is usually found in telephone networks and cables.
Comparison of Baseband and Broadband transmission (only for information)

## Slide 142
Ethernet Standards
Ethernet: It is a LAN protocol that is used in Bus and Star topologies and implements CSMA/CD as the medium access method
Original (traditional) Ethernet developed in 1980 by three companies: Digital, Intel, Xerox (DIX).
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers. Current version is called IEEE Ethernet
Basic frame format which is required for all MAC implementation is defined in IEEE 802.3 standard

## Slide 143
MAC or Ethernet address
A MAC address (media access control address) is a 12-digit hexadecimal number assigned to each device connected to the network.
Primarily specified as a unique identifier during device manufacturing, the MAC address is often found on a device's network interface card (NIC).
MAC addresses are also referred to as Ethernet addresses but multiple types of networks use MAC addressing, including Ethernet, Wi-Fi, and Bluetooth
MAC addresses are used to identify a device on the network.
A MAC address is responsible for local identification and an IP address for global identification.

## Slide 144
MAC addresses or Ethernet address
Traditional MAC addresses are 12-digit (6 bytes or 48 bits) hexadecimal numbers
The leftmost six digits (24 bits), called a prefix, are associated with the adapter manufacturer (M)
Each vendor registers and obtains MAC prefixes as assigned by the IEEE
For example, the prefixes 00:13:10, 00:25:9C, and 68:7F:74 (plus others) belong to Linksys (Cisco Systems).
The rightmost digits of a MAC address represent an identification number for the specific device (S).
Among all devices manufactured with the same vendor prefix, each is given a unique 24-bit number

## Slide 145
MAC addresses or Ethernet address
  Six bytes = 48 bits
  Flat address not hierarchical
  Burned into the NIC ROM
Examples of a unicast and a multicast MAC address
MAC address: 4A:30:10:19:10:1A
First Byte = 4A = 0100 1010
Last bit = 0
Its unicast address
MAC address: 01:00:5E:00:01:01
First Byte = 01 = 0000 0001
Last bit = 1
Its multicast address

## Slide 146
802.3 MAC frame
Basic frame format which is required for all MAC implementation is defined in IEEE 802.3 standard.

## Slide 147
802.3 MAC frame
PREAMBLE – Ethernet frame starts with a 7-Bytes Preamble. This is a pattern of alternative 0’s and 1’s which indicates starting of the frame and allow sender and receiver to establish bit synchronization. PRE (Preamble) indicates the receiver that frame is coming
Start of frame delimiter (SFD) – This is a 1-Byte field that is always set to 10101011. SFD indicates that upcoming bits are starting the frame, which is the destination address. The SFD warns station or stations that this is the last chance for synchronization.
Destination Address – This is a 6-Byte field that contains the MAC address of the machine for which data is destined.
Source Address – This is a 6-Byte field that contains the MAC address of the source machine. As Source Address is always an individual address (Unicast), the least significant bit of the first byte is always 0.

## Slide 148
802.3 MAC frame
Length – Length is a 2-Byte field, which indicates the length of the entire Ethernet frame. This 16-bit field can hold a length value between 0 to 65534, but length cannot be larger than 1500 Bytes because of some own limitations of Ethernet.
Data – This is the place where actual data is inserted, also known as Payload. Both IP header and data will be inserted here if Internet Protocol is used over Ethernet. The maximum data present may be as long as 1500 Bytes.
Cyclic Redundancy Check (CRC) – CRC is 4 Byte field. This field contains a 32-bits hash code of data, which is generated over the Destination Address, Source Address, Length, and Data field. If the checksum computed by destination is not the same as sent checksum value, data received is corrupted.

## Slide 149
Ethernet evolution through four generations

## Slide 150
Categories of traditional Ethernet

## Slide 151
Standard Ethernet topology

## Slide 152
Fast Ethernet
1. Upgrade the data rate to 100 Mbps.
2. Make it compatible with Standard Ethernet.
3. Keep the same 48-bit address.
4. Keep the same frame format
media: twisted pair (CAT 5) or fiber optic cable (no coax)
Star-wire topology- Similar to 10BASE-T
CAT 3
CAT 5

## Slide 153
Fast Ethernet Topology

## Slide 154
Gigabit Ethernet
1. Upgrade the data rate to 1 Gbps.
2. Make it compatible with Standard or Fast Ethernet.
3. Use the same 48-bit address.
4. Use the same frame format.
5. Keep the same minimum and maximum frame lengths.
6. Support auto-negotiation as defined in Fast
7. Ethernet Operates in full/half duplex modes mostly full duplex

## Slide 155
Gigabit Ethernet Topologies

## Slide 156
Thank You
Any Questions

## Slide 157
Categories of unshielded twisted-pair cables